# Command Language
The Ski command language is simple, efficient, and easy to learn. It consists of commands you can invoke from the keyboard or from a command file (see "" on page ). Each command is given with an appropriate set of arguments (some optional) to further qualify the command. Commonly-used commands may be abbreviated as described in "" on page and commands may be repeated easily. A limited on-line help facility (the help command) is provided for quick reference. This chapter presents the syntax of the command language. Information about specific commands (command semantics) is in later chapters and in "" on page .
## Command Entry
xski and ski provide similar mechanisms for controlling the simulator. Both provide for direct keyboard entry of commands. In addition, xski offers buttons, menus, and the Command History to minimize typing, as described in "" on page , and ski provides the command repetition mechanism for the same purpose, as described in "" on page . You give a command to Ski by typing the command name at the keyboard followed by operands and the enter/return key. (Use the help command to see a menu of available commands or help followed by the command name to see the command syntax.) xski displays the command you typed in the Command area of the Main Window. ski displays the command in the Command Window at the bottom of the screen following the * prompt. Commands are case sensitive. When you hit the enter/return key, Ski acts on your command and updates the screen to reflect any changes caused by the command. For example, the command
db
causes the Data Window to show the contents of lower addresses in memory.
## Command Arguments
Some commands, such as save, require additional information. If you don't provide the information, Ski displays an error message. Some commands have optional arguments. As described in "" on page , command summaries in this manual show optional arguments surrounded by square brackets [like this]. If you don't specify an optional argument, Ski uses a suitable default value. For example,
pf 3
causes the Program Window to advance three bundles after the last bundle in the Program Window, while
pf
alone moves the Program Window ahead one windowful. Some arguments can be supplied in a list, one or more times; these are shown by putting a plus sign ("+") after the argument name like this+. For example, the syntax description for the =1 command is:
=1 address_or_symbol value+
which suggests that the command
=1 __data_start 12 56 90 cd
assigns the hexadecimal values 12, 56, 90, and cd to the four bytes starting at the location specified by the symbol __data_start. Brackets and plus signs can be combined, [like this]+, to signify optional arguments that can be supplied zero or more times.
## Command Sequences, Repetition, and Abbreviation
You can type multiple commands on a single command line by separating the individual commands with semicolons (";"). This is called a "command sequence". Command sequences make re-executing a series of commands easy, using the Command History mechanism of xski (see "" page ) or the command repetition mechanism of ski (see "" on page ). For example, you might want to repeatedly execute the commands "step 100" and "eval my_buffer". This pair of commands would execute one hundred instructions and then print the value of (your) variable named "my_buffer". By combining these two commands into one command sequence, i.e., "step 100 ; eval my_buffer", you can use the Command History or command repetition mechanism to run these commands over and over. (The spaces around the semicolon are optional but improve readability.)
There is no grouping construct in Ski. This can be important when you write command files: when you want to execute commands conditionally using the if command, you cannot use the semicolon to group several commands into the "then" or "else" clauses. Instead, you must use labels and the goto command. The "" on page discusses command files in depth.
Most commands may be abbreviated, some to a single letter. A command may be abbreviated to the shortest prefix which is not also a prefix of a command which precedes it in the command menu. (See "" on page .)
## Argument Specification
The arguments which are given with commands are, in general, obvious and natural. The description which follows should clarify those cases which are not. The terms defined here are used in the command summaries throughout the remainder of this manual.
### Numeric Arguments
Many commands accept numeric arguments. The argument may be an address, a value, an execution count, or some other variable which is best expressed numerically.
#### Numbers and Counts
Some commands take arguments that are naturally expressed in hexadecimal: addresses, for example. Other commands take arguments that are naturally expressed in decimal, such as the number of instructions to simulate with the step command. To make using Ski easier, some Ski commands default to interpreting their arguments as (hexadecimal) numbers and some default to interpreting their arguments as (decimal) counts. You can always override the default interpretation by specifying a radix override, as described below.
Hexadecimal digits may be upper or lower case. The default radix may be overridden by preceding the number or count with 0D or 0d for decimal, 0X or 0x for hexadecimal, 0O or 0o (zero-oh) for octal, and 0B or 0b for binary. Since both the decimal and binary prefixes look like hexadecimal, hexadecimal values such as 0d600000 and 0b100000 must be specified either with an explicit hexadecimal prefix, as in 0x0d600000 and 0x0b100000, or without the leading 0, as in d600000 and b100000.
#### Expressions
Wherever a number or count is needed, you can use a numeric expression instead, with parenthesis as needed for grouping. No spaces are allowed in an expression. In an expression whose result will be used as a number, numbers not preceded by a radix override are assumed to be hexadecimal. If the result will be used as a count, numbers not preceded by a radix override are assumed to be decimal. For example, the step command expects a count operand, so the command
step r0+10
steps (decimal) ten instructions. On the other hand, the pj command expects an address operand, which is a number, so the command
pj r0+10
displays (hexadecimal) address 0x10 in the Program Window. (r0 is hardwired to always return a zero when read.)
The available operators are shown in order from higher to lower precedence in Table 1: Ski Simulator Arithmetic and Logic Operators. Operator precedence rules follow the C language rules.
Operator	Description
( )	group operators with operands
! ~ + - *	opposite truth value, logical one's complement, unary plus, unary minus, dereference: treat as an address and read eight bytes
* /	multiply, divide
+ -	add, subtract
<< >>	logical left shift, logical right shift
< <= > >=	less than, less than or equal to, greater than, greater than or equal to
== !=	equal to, not equal to
&	bitwise and
^	bitwise exclusive or
|	bitwise or
&&	logical and
||	logical or

Table 1: Ski Simulator Arithmetic and Logic Operators

As an example, in xski,
eval 64 0d64 0o64 0b100000 *main ~(((0D1234+0X10EF0)*4)<<6)+0B10001001
prints the values of the six expressions in the Main Window, as shown in Illustration 1: xski Evaluating Expressions. The first expression is taken as a hexadecimal number, the second as a decimal number, the third as an octal number, and the fourth as a binary number. The fifth expression is the value at the location specified by the symbol "main" (the first 64 bits of the code bundle at that location), and the sixth expression is the result of some arithmetic.
Illustration 1: xski Evaluating Expressions

#### Addresses
An address is specified by a 64 bit hexadecimal number. For example, the command
pj 1000
repositions ("jumps") the Program Window to address 0x1000. As discussed in "" on page , Ski supports generic addresses in application-mode programs (that is, the concept of "virtual memory" doesn't apply to application mode programs), and physical and virtual addresses in system-mode programs. For system-mode programs, the psr.dt and psr.it bits control whether Ski interprets addresses as physical or virtual. In some cases, you may need to change the value of one or both of these bits temporarily, so that Ski will interpret addresses the way you want. You should restore the bit values before resuming simulation, of course. You can set the psr.dt bit with the Ski command "= psr.dt 1" and clear the bit with "= psr.dt 0". The corresponding commands for the psr.it bit are "= psr.it 1" and "= psr.it 0", respectively.
Addresses may be computed using expressions. For example, the command
dj 1000+0d50
repositions ("jumps") the Program Window to address 1032, because 1000 (hexadecimal) added to 50 (decimal) is 1032 (hexadecimal). Address expressions are particularly useful in symbolic constructs, as described below.
### Symbolic Arguments
A symbol is a sequence of characters (a "name"). Examples of symbols are program-defined symbols, registers, internal variables, labels, and filenames. Arguments may (and sometimes must) be expressed symbolically.
#### Program-Defined Symbols
A program-defined symbol is an identifier which can be used as a mnemonic for a memory location. Program-defined symbol names are defined in the executable file for the program being simulated. Some symbols are common, well-known names (e.g. printf, main), and others are defined by the programmer (e.g. foo, bar). The symlist command shows you the symbols sorted by address, as Illustration 2: xski's Symbol List Window shows.

Illustration 2: xski's Symbol List Window

#### Registers
A register name is a predefined mnemonic for a processor register. The general registers, for example, are referred to as r0, r1, ..., r127. (The register names Ski recognizes are listed in "" on page .) For example, the command
= r31 ip
assigns the value contained in the ip register to general register 31. (For a description of the = command, see "" on page .) Wherever the simulator expects you to supply a numeric argument, you can use a register instead. You may only refer to currently-visible registers, according to the stacking and rotation mechanisms of the IA-64 architecture.
#### Internal Variables
The simulator provides internal variables for you to use in command files (see "" on page ). These internal variables are read-only; you cannot change their values. You can refer to an internal variable in any context where you could refer to an IA-64 register. Ski has four internal variables:
$cycles$
The total number of "virtual cycles" simulated. A virtual cycle is a cycle on a machine with an very large number of execution units and very fast memory; a real IA-64 processor may take more cycles. In a command file, you might use this variable to gather statistics about the efficiency of a particular compiler optimization algorithm. The value of $cycles$ is always equal to the value of $insts$ for IA-32 programs.
$exited$
The value 0 until the simulated program exits. Then the variable takes the value 1. In a command file, you would use $exited$ to detect a program termination. Program termination is defined for IA-64 application-mode programs as a call to the exit() function or the receipt of an unhandled signal. For IA-64 system-mode programs, normal termination is defined to be a call to the Simulator System Call exit function or execution of BREAK 0 instruction. This variable is not supported for IA-32 programs in application-mode or system-mode. (See "" on page for details on these modes.)
$heap$
This variable has meaning only for IA-64 programs running in application-mode, as described in "" on page . $heap$ marks the address past the "far end" of the simulated heap, that is, the end farthest from the end of the data section. The heap starts at the first sixteen-byte-aligned address after the data section. Ski updates the $heap$ variable as the program being simulated malloc's memory (for programs written in C; adapt accordingly for other programming languages). You can use the $heap$ variable to debug wild pointer problems: if your program has a pointer that allegedly points to a malloc'ed data structure, but the pointer value exceeds $heap$, the pointer is invalid. For system-mode programs and IA-32 programs, this variable is meaningless, as there is no malloc support.
$insts$
The number of instructions that have been simulated so far (including any faulting instructions, for programs running in system-mode, described in "" on page . In a command file, you might use this variable to stop simulation after a certain number of instructions. The value of $insts$ is always equal to the value of $cycles$ for IA-32 programs.
#### Labels
Labels (see "" on page ) are names which consist of an alpha (upper or lower case alphabetic, $, or _), followed by a sequence of alphas or digits (e.g., abc123, $foo_bar, etc.) and ending with a colon (":"). They may be up to 132 characters long. Labels are used in command files as targets of the goto command.
#### Filenames
Filenames are subject to the restrictions of the underlying Linux operating system. Ski performs tilde ("~") expansion: if you provide a pathname whose first word starts with a tilde, Ski assumes the word is a username and tries to replace it (and the tilde) with the user's home directory. For example, "~david/hello" might be expanded to "/home/david/hello".
### Resolving Ambiguous Symbols and Numbers
Some character sequences can be interpreted in more than one way. For example, the character sequence "b3" can be interpreted as a branch register, a program-defined symbol, or a hexadecimal number. To resolve the ambiguity, Ski looks first in its symbol tables for program-defined symbols and internal variables (which includes register names). If a match is found, the matching value is used, otherwise the character sequence is taken as a number. You can force the numeric interpretation by putting a "0x" or "0X" prefix in front of the number, such as "0xb3". It is undefined whether Ski searches the symbol table for program-defined symbols before or after the internal variable symbol table. Because of this, it is wise to avoid naming global variables and functions with names duplicating any of Ski's internal variables. In practice, this means you should avoid using register names as names of variables and functions in your programs.